## Slide 1
Computer Networks
Topic 11:
Voice over IP and Video Conferencing

## Slide 2
Computer Networks
Topic 11 – Lecture 1: Voice over IP (VoIP)

## Slide 3: Scope and Coverage
Voice over IP and Video Conferencing Topic 11 - 11.3
This topic will cover:
Voice over IP (VoIP)
Installing and configuring voice networks and video conferencing

## Slide 4: Learning Outcomes
Voice over IP and Video Conferencing Topic 11 - 11.4
By the end of this topic, students will be able to:
Describe the components of a VoIP system
Install and configure a VoIP system
Install and configure a web-based video conferencing solution

## Slide 5: Communication Over the Internet
Voice over IP and Video Conferencing Topic 11 - 11.5
Typical transmission over IP in the early days
  Data
  Simple web pages
Media transmission over IP today
  Audio
    Telephony (VoIP), live radio, etc.
  Image
    Gallery viewers, CAD drawings, etc.
  Video
    Streaming video, “live” TV, etc.

## Slide 6: What is VoIP?
Voice over IP and Video Conferencing Topic 11 - 11.6
The use of IP networks, namely the LAN (internal network) and WAN (the Internet) to carry voice communications
Voice was originally carried over circuit switched networks (and still is)
  PSTN
Internet that was originally designed to carry computer data is also used to carry voice.
  A packet switched network

## Slide 7: Basic VoIP Functions
Voice over IP and Video Conferencing Topic 11 - 11.7
Signalling
Database services
  Mapping addresses (IP to Phone numbers) etc.
Call connect and disconnect (bearer control)
Codec operations
  For encapsulating voice signals into data packets.
  For decoding the packets and transforming them back into a voice signal.

## Slide 8: What is a Codec?
Voice over IP and Video Conferencing Topic 11 - 11.8
A device or software that is used to compress or decompress a digital media file, such as an audio file
A codec can consist of two components:
  An encoder performs the compression (encoding) function.
  A decoder performs the decompression (decoding) function.

## Slide 9: VoIP Components
Voice over IP and Video Conferencing Topic 11 - 11.9
Servers
– For processing calls and managing interactions with the telephone network, etc.
End-point devices, such as telephone handsets
Media and VoIP gateways
IP network

## Slide 10: VoIP Gateways & Gatekeepers
Voice over IP and Video Conferencing Topic 11 - 11.10
Gateway equipment performs the task of allowing non-IP equipment to talk to IP equipment.
Gatekeepers manage the calls within a particular zone.

## Slide 11: Issues
Voice over IP and Video Conferencing Topic 11 - 11.11
Latency
Jitter
Bandwidth
Packet loss
Reliability
Scalability
Security
Features
Interoperability
Switch over cost

## Slide 12: Latency
Voice over IP and Video Conferencing Topic 11 - 11.12
The time taken for a packet to arrive at its destination
This is affected by:
  Packet switching overhead
  The amount of traffic on the network
Latency may result in voice synchronisation problems
  Gaps in transmission

## Slide 13: Jitter
Voice over IP and Video Conferencing Topic 11 - 11.13
The delay experienced in receiving a packet when a packet is expected to arrive at a certain time
  If you send a sequence of packets from point A to point B, each of the packets will need a slightly different time to reach the destination.
  The varying transit times are not an issue if you are downloading a web page, but they matter if you wish to transmit a stream of real-time data, such as voice, video, etc.

## Slide 14: Bandwidth
Voice over IP and Video Conferencing Topic 11 - 11.14
Bandwidth is shared between voice and computer data on the network.
Certain bandwidth may have to be allocated for voice communication on a network.
What happens when many VoIP calls are occurring at the same time?

## Slide 15: Packet Loss
Voice over IP and Video Conferencing Topic 11 - 11.15
Packet loss in unavoidable
Voice transmission can only tolerate minimal packet loss.
– It should not distort the audio.
Packet loss on VoIP is similar to when a call on a
cell/mobile phone begins to “break-up”.
This results in the receiver missing parts of the conversation.

## Slide 16: Reliability
Voice over IP and Video Conferencing Topic 11 - 11.16
The reliability of the network has an impact on the telephony service.
– In the analogue telephone industry, reliability of 99.999 percent uptime is required.
Require reliable network connection with sufficient bandwidth.

## Slide 17: Scalability
Voice over IP and Video Conferencing Topic 11 - 11.17
Ability to add more telephony equipment as the company grows.
Network bandwidth and other issues may have an effect on scalability.
Can the network deal with the extra traffic?

## Slide 18: Security
Voice over IP and Video Conferencing Topic 11 - 11.18
VoIP typically uses the Internet.
It is, therefore, vulnerable to the same type of security risks as other Internet traffic:
  Hacking
  Denial of service
  Eavesdropping

## Slide 19: Features
Voice over IP and Video Conferencing Topic 11 - 11.19
In order to compete with traditional telephony, VoIP telephony needs to match and, in the long run, exceed the features provided by the PSTN.
  Call waiting
  Conference calls
Already has extra features:
  Video calls
  Free! (in some instances)

## Slide 20: Interoperability
Voice over IP and Video Conferencing Topic 11 - 11.20
IP telephony equipment manufactured by different vendors must be able to talk to each other.
Without standardised quality of service mechanisms, businesses would need to buy all the equipment and the QoS server from the same manufacturer.
VoIP seems to be divided among multiple vendors with reluctance to establish interoperability.

## Slide 21: Switch Over Costs
Voice over IP and Video Conferencing Topic 11 - 11.21
Switching from a more traditional telephone system to VoIP may involve costs.
  Equipment
  Extra bandwidth
Savings are likely on cost of calls.

## Slide 22: Benefits of VoIP
Voice over IP and Video Conferencing Topic 11 - 11.22
Issues have been resolved to an acceptable level
Usually reduces costs
Utilises “spare” bandwidth
No separation of data and voice networks
“Extras” are free of charge:
  Conference calling
  Call forwarding
  Automatic redial
  Caller ID

## Slide 23
Computer Networks
Topic 11 – Lecture 2:
VoIP Systems & Video Conferencing

## Slide 24: What is Needed to Set Up VoIP?
Voice over IP and Video Conferencing Topic 11 - 11.24
An existing broadband Internet connection
A VoIP-compatible phone
A VoIP provider
Alternatively, use a software solution.
– E.g. Skype

## Slide 25: Broadband Internet Connection
Voice over IP and Video Conferencing Topic 11 - 11.25
Essential for telephone-quality audio
Good connection speed
If you expect to make a lot of calls, make sure that your plan has a suitable usage limit.
Check with your ISP – they may also offer a VoIP service and it may be possible to save on both bills by bundling.

## Slide 26: VoIP Compatible Phone
Voice over IP and Video Conferencing Topic 11 - 11.26
Telephone handsets specifically designed to work over VoIP can be purchased.
Plug directly into your Internet connection
ATA adapter can be purchased, which allows plugging of existing telephone into Internet connection.
Both require a router or network hub - can be wired or wireless
Some newer routers incorporate VoIP adapters.

## Slide 27: VoIP Provider
Voice over IP and Video Conferencing Topic 11 - 11.27
Choose a provider and plan that suits your needs:
  Price
  Additional features, e.g. multiple numbers for incoming calls
There are many providers available in many countries.
Not available in some countries

## Slide 28: Software VoIP
Voice over IP and Video Conferencing Topic 11 - 11.28
Your computer can be used as a VoIP phone.
Needs a VoIP software package
– the most popular of which is Skype
Allows you to conduct VoIP calls through a microphone and headphones/speakers or a cheap USB phone
Calling other VoIP software users is usually free and calls to other phones are at low VoIP rates.

## Slide 29: VoIP Protocols
Voice over IP and Video Conferencing Topic 11 - 11.29
There are both open and proprietary protocols.
Open protocols are in the public domain.
Proprietary protocols relate to one vendor.
Common protocols in VoIP are:
– H.323
  Real-time Transport Protocol (RTP)
  Session Initiation Protocol (SIP)
  Skype protocol – a proprietary protocol
Often, combinations of protocols are used.

## Slide 30: H.323
Voice over IP and Video Conferencing Topic 11 - 11.30
A multimedia conferencing protocol, which includes voice, video, and data conferencing, for use over packet-switched networks
A framework of how other protocols fit together, including:
  H.245 - the protocol used to control establishment and closure of media channels within the context of a call.
  RTP/RTCP - to transmit audio over IP networks.
  X.691 - the Packed Encoding Rules (PER) used to encode messages for transmission on the network.

## Slide 31: Real-Time Transport Protocol
Voice over IP and Video Conferencing Topic 11 - 11.31
A standardised packet format for delivering audio and video over IP networks
Standard defines a pair of protocols:
  RTP is used for transfer of multimedia data.
  RTCP is used to periodically send control information and QoS parameters.
Provides jitter compensation and detection of out of sequence packets
Supports data transfer to multiple destinations

## Slide 32: Session Initiation Protocol
Voice over IP and Video Conferencing Topic 11 - 11.32
Very flexible, lightweight protocol for making multimedia calls
SIP is an end-to-end, client-server, extensible, text- based protocol.
The design is based upon HTTP and SMTP.
SIP runs on any transport protocol (TCP, UDP).
Provides user location and session management
Does not provide services itself

## Slide 33: Skype Protocol
Voice over IP and Video Conferencing Topic 11 - 11.33
Skype is a proprietary Internet telephony network based on peer-to-peer architecture, whereas many VoIP solutions are client-server based.
The protocol's specs are not publicly available.
The Skype network is not interoperable with most other VoIP networks without proper licensing from Skype.
Signaling and voice data is encrypted.
Skype can be used for video calls.

## Slide 34: Video Conferencing
Voice over IP and Video Conferencing Topic 11 - 11.34
Two or more participants at different sites using computer networks to transmit audio and video data
Each participant has a video camera, microphone, and speakers mounted on a computer.
Voices are carried over the network and delivered to the other participant's speakers; whatever images appear in front of the video camera, appear in a window on the other participant's monitor.

## Slide 35: Video Conferencing Advantages
Voice over IP and Video Conferencing Topic 11 - 11.35
Less expensive than travelling
Easy access to experts
Direct access to training, mentoring, etc.
More personal than a telephone call
Allows communication on all levels, including body language
Saves time and money

## Slide 36: Components
Voice over IP and Video Conferencing Topic 11 - 11.36
Codec
Video input device
Video output device
Audio input device
Audio output device
Data transfer network
Computer

## Slide 37: Videoconferencing Systems
Voice over IP and Video Conferencing Topic 11 - 11.37
Web camera videoconferencing systems add on to personal computers
  Connected by VoIP networks
  Lowest direct cost
  Quality of service can range from low to very high
Dedicated videoconferencing systems:
  Mid range cost
  Utilise multipoint control units
  Quality of service can vary from moderate to high

## Slide 38: Multipoint Control Units
Voice over IP and Video Conferencing Topic 11 - 11.38
A device commonly used to bridge videoconferencing connections
An endpoint on a LAN that provides the capability for 3 or more terminals and gateways to participate in a multipoint conference
Consists of:
  A mandatory Multipoint Controller (MC)
  Optional Multipoint Processors (MPs)

## Slide 39: Telepresence Systems
Voice over IP and Video Conferencing Topic 11 - 11.39
Highest capabilities
Highest cost
Can involve especially built teleconference rooms with very high levels of audio and video fidelity
When the proper type and capacity transmission lines are provided between facilities, the quality of service reaches state-of-the-art levels.

## Slide 40: References
Voice over IP and Video Conferencing Topic 11 - 11.40
Tanenbaum, A.S. & Weatherall, D.J. (2010). Computer Networks, 5th edition. Pearson Education.
Austerberry, D. (2004). The Technology of Video and Audio Streaming, 2nd edition. Focal Press.

## Slide 41: Topic 11 – Voiceover IP and Video Conferencing
Voice over IP and Video Conferencing Topic 11 - 11.41
Any Questions?