## Slide 1
Computer Networks
Topic 3:
Wireless Networking Standards

## Slide 2
Computer Networks
Topic 3 – Lecture 1: Wireless Devices

## Slide 3: Scope and Coverage
Wireless Networking Standards Topic 3 - 3.3
This topic will cover:
Wireless devices
Wireless networking standards
Issues for wireless networks
Wireless networking protocols

## Slide 4: Learning Outcomes
Wireless Networking Standards Topic 3 - 3.4
By the end of this topic, students will be able to:
Explain the function and rationale of wireless networking standards
Explain a range of contemporary wireless standards and their relevant applications

## Slide 5: Wireless Networks
Wireless Networking Standards Topic 3 - 3.5
Wireless Networks are networks in which electromagnetic waves carry the signal over part or all of the communication path.
This is in contrast to networks that utilise physical media, such as fibre-optic cable, coaxial cable, etc.

## Slide 6: Advantages of Wireless
Wireless Networking Standards Topic 3 - 3.6
Increased mobility
Increased flexibility
Convenience
Opportunities to provide new services

## Slide 7: History of Wireless
Wireless Networking Standards Topic 3 - 3.7
Wireless technology has been around for a few decades.
Take up was initially slow:
  Low data transfer rates
  Little interoperability between different devices
  High cost
Great increase in number of wireless networks due to standardisation, greater speeds and reduced costs

## Slide 8: Wireless Devices
Wireless Networking Standards Topic 3 - 3.8
Computer peripherals
Wireless LANs
Bluetooth devices
RFID
Many others, e.g. mobile telephones, TV remote control, GPS, etc.

## Slide 9: Wireless Computer Peripherals - 1
Wireless Networking Standards Topic 3 - 3.9
Devices include mouse, printer, keyboard, scanner, etc.
Can allow multiple devices to use the same peripheral
Removes the need for cumbersome cables
Limited flexibility by operating a little distance away from the PC

## Slide 10: Wireless Computer Peripherals - 2
Wireless Networking Standards Topic 3 - 3.10
Use two technologies:
  Infrared (IR) is cheaper, has less interference, but requires direct optical contact between the peripheral and receiver.
  Radio frequency (RF) works in all angles relative to the receiver, even with objects between the peripheral and receiver, but it is more expensive.

## Slide 11: Wireless LAN (WLAN)
Wireless Networking Standards Topic 3 - 3.11
Wireless networking relies on a broadcast signal.
Suitably configured devices contain receivers that pick up and understand the broadcast signal.
Devices can process data and broadcast signals as well.

## Slide 12: WLAN Components - 1
Wireless Networking Standards Topic 3 - 3.12
Wireless Adapters (WA)
  Capable of transmitting and receiving wireless digital signals and are usually contained in the user device
  Modern PCs, laptops, smartphones, etc. all come with a wireless adapter.

## Slide 13: WLAN Components - 2
Wireless Networking Standards Topic 3 - 3.13
Access Points (AP)
  Acts as a base station that receives and transmits signals via radio waves
  It provides the link between the devices and the network.

## Slide 14: Hotspots
Wireless Networking Standards Topic 3 - 3.14
A wireless client may be any device (computer or peripheral) designed to use the same wireless protocol as the access point.
A client must be in range of the access point.
The area within range of an AP is known as a
“hotspot”.
Overlapping hotspots allow a wireless network to cover a wide area.

## Slide 15: Bluetooth
Wireless Networking Standards Topic 3 - 3.15
A short range radio link with a range of around 10 metres
Allows a number of devices to link together in an ad-hoc network
Does not require line of sight
Can provide communication links between phones, PDAs, computers, peripherals, etc
Can transmit voice and data

## Slide 16: Piconets
Wireless Networking Standards Topic 3 - 3.16
The Bluetooth ad-hoc networks
Can have up to eight devices on the same piconet
Each piconet is synchronised to the clock of one device on it (the master).
Other devices are slaves
Several piconets may be active in the same location.
Each device can be a part of several piconets, but only master of one.

## Slide 17: RFID Tags
Wireless Networking Standards Topic 3 - 3.17
A radio frequency identification tag is a small object that is attached to another object in order to identify it via radio waves
Has two main components:
  An integrated circuit that modulates and demodulates a radio signal, stores data and processes information
  Antenna for transmitting/receiving

## Slide 18: RFID Tag Uses
Wireless Networking Standards Topic 3 - 3.18
A wide range of uses including:
  Passports
  Travel cards
  Wildlife tracking
  Stocktaking in shops

## Slide 19: Other Wireless Devices
Wireless Networking Standards Topic 3 - 3.19
There are many devices in common use that are wireless:
  Mobile telephones
  TV
  Satellite communications
  Pagers (e.g. hospital)
  Remote alarms
  GPS
  Remote controls (TV, model aircraft)
  Two-way radio …..

## Slide 20
Computer Networks
Topic 3 – Lecture 2:
Wireless Networking Standards

## Slide 21: Wireless Standards
Wireless Networking Standards Topic 3 - 3.21
IEEE 802.11 series – Wireless LAN
Bluetooth/IEEE 802.15 - Wireless Personal Area Network
IEEE 802.16 - Wireless Metropolitan Area Networks
IEEE 802.20 - Mobile Broadband Wireless

## Slide 22: Why Do We Need Standards?
Wireless Networking Standards Topic 3 - 3.22
There are a number of key reasons for creating and adhering to standards for wireless networking.
Interoperability
  Different devices work together
Many equipment manufacturers
  Customers can switch for better price or features
Allocation of frequencies
  The radio wave spectrum is used for many applications

## Slide 23: The IEEE 802.11 standards
Wireless Networking Standards Topic 3 - 3.23
WLAN or WiFi
Wireless LAN Media Access Control and Physical Layer specification
Contains a number of revisions and interpretations:
– 802.11a,b,g,etc. are amendments to the original
802.11 standard
Products that implement 802.11 standards must pass tests and are referred to as "Wi-Fi certified”.

## Slide 24: The Original IEEE 802.11
Wireless Networking Standards Topic 3 - 3.24
Data rates of up to 2 Mbps
Uses Frequency Hopping Spread Spectrum (FHSS) or Direct Sequence Spread Spectrum (DSSS) signalling techniques
2.4 GHz frequency range

## Slide 25: IEEE 802.11 Revisions - 1
Wireless Networking Standards Topic 3 - 3.25
802.11a
  Uses Orthogonal Frequency-Division Multiplexing (OFDM)
  Enhanced data speed to 54 Mbps
  5 GHz frequency range
802.11b
  Added higher data rate modes to DSSS
  Data speeds up to 11 Mbps
  22 MHz Bandwidth yields 3 non-overlapping channels in the frequency range of 2.4 GHz frequency band.

## Slide 26: IEEE 802.11 Revisions - 2
Wireless Networking Standards Topic 3 - 3.26
802.11d
  Enhancement to 802.11a and 802.11b allows for global roaming
  Particulars can be set at Media Access Control
(MAC) layer
802.11e
  Enhancement to 802.11 includes quality of service features
  Facilitates prioritisation of data, voice, and video transmissions

## Slide 27: IEEE 802.11 Revisions - 3
Wireless Networking Standards Topic 3 - 3.27
802.11g
  Extends the maximum data rate in the 2.4 GHz band, permits interoperation with 802.11b devices
  Uses OFDM
  54 Mbps, with fall-back speeds that include the b speed
802.11h
  Deals with interference
802.11i
  Deals with security

## Slide 28: IEEE 802.11 Revisions - 4
Wireless Networking Standards Topic 3 - 3.28
802.11n
  High speed WLAN
  Can theoretically operate at bandwidths up to 600 Mbps
  Applications supporting 100 Mbps using the TCP/IP protocol are available.
  Uses Multiple-Input Multiple-Output (MIMO) technology
  Uses 5 GHz band

## Slide 29: Which Version?
Wireless Networking Standards Topic 3 - 3.29
Most modern wireless routers will support 802.11n plus 802.11b and 802.11g
Older routers may only support 802.11b and 802.11g
Higher speed networks should use 802.11n

## Slide 30: IEEE 802.15/Bluetooth
Wireless Networking Standards Topic 3 - 3.30
IEEE 802.15 covers Wireless Personal Area
Networks (WPAN).
Working Group1 (IEEE 802.15.1) is a standard based upon Bluetooth version 1.1.
The Bluetooth Special Interest Group (SIG) is a separate non-profit organisation that oversees the Bluetooth standards.
The Bluetooth SIG and IEEE are not related
– No IEEE standards match recent Bluetooth standards

## Slide 31: Bluetooth
Wireless Networking Standards Topic 3 - 3.31
Open wireless technology standard
Exchanges data over short distances
Uses short wavelength radio transmissions
Used in fixed and mobile devices
Creates Personal Area Networks (PANs)

## Slide 32: Bluetooth Range
Wireless Networking Standards Topic 3 - 3.32
The range is specific to the application.
The Core Specification states a minimum range of 10 metres or 30 feet.
However, there is no set limit.
Manufacturers are allowed to tune their devices to provide the range they require.

## Slide 33: Bluetooth Spectrum
Wireless Networking Standards Topic 3 - 3.33
Operates in the unlicensed industrial, scientific and medical (ISM) band
Frequencies 2.4 to 2.485 GHz are used
Uses a spread spectrum, frequency hopping, full- duplex signal at a nominal rate of 1600 hops/sec.
The 2.4 GHz ISM band is available and unlicensed in most countries.

## Slide 34: Bluetooth Interference
Wireless Networking Standards Topic 3 - 3.34
Adaptive frequency hopping (AFH) reduces interference between wireless technologies sharing the 2.4 GHz spectrum.
The technology detects other devices in the spectrum and avoids the frequencies they are using.

## Slide 35: Bluetooth Range
Wireless Networking Standards Topic 3 - 3.35
Range depends on class of radio used:
  Class 3 radios have a range of up to 1 metre or 3 feet
  Class 2 radios, most commonly found in mobile devices, have a range of 10 metres or 33 feet
  Class 1 radios, used primarily in industrial devices, have a range of 100 metres or 300 feet

## Slide 36: IEEE 802.16
Wireless Networking Standards Topic 3 - 3.36
Mobile Broadband Wireless Access
Also known as WiMAX (from "Worldwide Interoperability for Microwave Access")
Provides up to 40 Mbps
Currently working on the IEEE 802.16m update
  Expected to offer up to 1 Gbps fixed speed
  Required for 4G networks

## Slide 37: WiMAX Usage
Wireless Networking Standards Topic 3 - 3.37
Provides mobile broadband or at-home broadband connectivity across whole cities or countries.
Deploying a WiMAX network has low cost in comparison to DSL or Fibre-Optic.
Can provide broadband in remote locations

## Slide 38: Comparison with WiFi
Wireless Networking Standards Topic 3 - 3.38
WiMAX covers many km and uses an unlicensed spectrum to provide access to a local network.
Wi-Fi is more popular in end user devices.
802.11 supports direct, ad hoc or peer-to-peer networking between end user devices without an access point, while 802.16 end user devices must be in range of the base station.

## Slide 39: IEEE 802.20
Wireless Networking Standards Topic 3 - 3.39
Mobile Broadband Wireless Access (MBWA)
Aims to enable worldwide deployment of interoperable mobile broadband wireless access networks, including:
  Mobile and ubiquitous Internet access
  Transparent support of Internet applications
  Access to enterprise intranet services
  Transparent access to infotainment and location services

## Slide 40: IEEE 802.20 Detail
Wireless Networking Standards Topic 3 - 3.40
Bandwidths of 5, 10, and 20 MHz
Peak data rates of 80 Mbps
Uses MIMO
Supports low-bit rates efficiently, carrying up to 100 phone calls per MHz
Allows network access whilst travelling at speeds of 250 km/h

## Slide 41
Computer Networks
Topic 3 – Lecture 3:
Issues for Wireless Networks

## Slide 42: Wireless Issues
Wireless Networking Standards Topic 3 - 3.42
There are a number of issues that may cause concern for those using radio frequencies for network media rather than physical cables, these include:
  Range
  Interference
  Security

## Slide 43: Range
Wireless Networking Standards Topic 3 - 3.43
The range where wireless signals can be reliably transmitted and received is a key parameter for a wireless network.
In ideal conditions, a WLAN can have a range of 300m or more.
Real world conditions are not ideal.
In an office/home, range can drop as low as 10m.

## Slide 44: Indoor Range
Wireless Networking Standards Topic 3 - 3.44
WLANs are normally implemented indoors and a number of factors will affect the range of the network:
  Building design
  Construction materials
  Room layout
  The location and type of other electrical devices

## Slide 45: Installation
Wireless Networking Standards Topic 3 - 3.45
Technically simple regarding installation and configuration
Installation does need to take into account the location of:
  access points
  networked devices
  obstacles

## Slide 46: Interference
Wireless Networking Standards Topic 3 - 3.46
Radio frequency signals can be negatively affected by other radio signals in the same frequency band.
There are two main sources of such signals:
  Reflected signals from the wireless network itself
  Other electrical equipment

## Slide 47: Multipath
Wireless Networking Standards Topic 3 - 3.47
Radio frequency signals can be affected by signals bouncing off building surfaces and other obstacles
Signals can come from multiple directions (multipath)
May cancel or reduce signal strength

## Slide 48: Eliminating Multipath
Wireless Networking Standards Topic 3 - 3.48
Most access appointments include software tools that analyse signal strength.
These can be used to test signal strength of networked computers.
Most networked equipment can be moved to improve signal strength.

## Slide 49: External Interference
Wireless Networking Standards Topic 3 - 3.49
Radio emissions from other devices using the same frequency band are a source of interference
There are particular industries where this is a problem
– Hospitals use a lot of monitoring equipment that may use the same frequency
Equipment may need to be isolated to prevent the interference.

## Slide 50: Security Issues
Wireless Networking Standards Topic 3 - 3.50
Security can be compromised in different ways from hard-wired networks.
Radio transmission cannot be limited to within the network premises.
Therefore, the transmitted signals can be intercepted by devices outside of a building and this data could include sensitive business or personal data.

## Slide 51: Drive–by Hacking
Wireless Networking Standards Topic 3 - 3.51
Any IEEE 802.11 receiving device using the relevant standard could pick up a transmitted signal.
A hacker could be located near a business premises and pick up these signals.
As the signals are broadcast, there would be no way of knowing that an unauthorised person had accessed the signal.

## Slide 52: Wired Equivalent Privacy (WEP)
Wireless Networking Standards Topic 3 - 3.52
The first major attempt to make wireless networks as secure as wired networks
Susceptible to eavesdropping
Has been deprecated by IEEE as it does not meet its security goals
Still widely in use

## Slide 53: WiFi Protected Access (WPA)
Wireless Networking Standards Topic 3 - 3.53
Brought in as an improvement on WEP
WPA is more secure and comes in two forms
  A form using pre-shared keys for home networks
  A more secure form using an authentication server for business networks
WPA has also been cracked and been replaced by WPA2 which is more secure.

## Slide 54: Bluetooth Security
Wireless Networking Standards Topic 3 - 3.54
There are a number of known security flaws with Bluetooth devices and these include:
  Bluejacking
  Bluesnarfing
  Bluebugging
  Bluetoothing

## Slide 55: Bluejacking
Wireless Networking Standards Topic 3 - 3.55
The hacker sends a phone contact or business card to another nearby phone.
The ‘name' field of the contact can be misused by
replacing it with a suggestive text.
This is equivalent to spam email since both are unsolicited messages displayed on recipients' end without consent.

## Slide 56: Bluesnarfing
Wireless Networking Standards Topic 3 - 3.56
Accesses or steals data like messages, such as a calendar or phone book from the target device.
There have been reports of the tools that use methods such as device address guessing and brute force in order to break-in, even when device is configured as ‘invisible‘.

## Slide 57: Bluebugging
Wireless Networking Standards Topic 3 - 3.57
The target device is controlled by the attacker who sends commands as if they had physical access.
Similar to a trojan

## Slide 58: Bluetoothing
Wireless Networking Standards Topic 3 - 3.58
Short range social networking
Harassment of individuals within range

## Slide 59: Securely Using Bluetooth
Wireless Networking Standards Topic 3 - 3.59
Keep devices in the disabled state, enable it only when needed
Keep the device in non-discoverable mode
Do not accept any unknown and unexpected request for pairing your device
Use non regular patterns as PIN keys
Keep a check of all paired devices and delete any paired device which you are not sure about
Register your device at the manufacturer site

## Slide 60
Computer Networks
Topic 3 – Lecture 4:
Wireless Networking Protocols

## Slide 61: Protocol Stacks
Wireless Networking Standards Topic 3 - 3.61
Wireless networks have layered protocol stacks like other networks.
We will not deal with the higher level layers.
We will examine protocol stacks and specific technologies of:
  WLAN
  Bluetooth

## Slide 62: WLAN Protocol Stack
Wireless Networking Standards Topic 3 - 3.62

## Slide 63: WLAN LLC & MAC Layers
Wireless Networking Standards Topic 3 - 3.63
LLC designed to provide the functionality of the High-Level Data Link Control protocol of
the standard TCP/IP protocol stack
LLC allows an 802.11 protocol stack to be grafted underneath any TCP/IP implementation with little or no change to the upper layers
MAC provides the same functions as in other protocol stacks

## Slide 64: WLAN PHY Layer
Wireless Networking Standards Topic 3 - 3.64
Original 802.11 standard defined three specific physical network protocols:
  An infrared communications standard
  A Direct-Sequence Spread Spectrum (DSSS) RF protocol
  A Frequency-Hopping Spread Spectrum
(FHSS) RF protocol
Later versions of the 802.11 standard redefined the physical layer to be DSSS only.

## Slide 65: Bluetooth Protocol Stack - 1
Wireless Networking Standards Topic 3 - 3.65

## Slide 66: Bluetooth Protocol Stack - 2
Wireless Networking Standards Topic 3 - 3.66
The bottom layer of the stack is the HCI, the Host Controller Interface
  This is the interface between the host (e.g. a computer) and the controller (e.g. a Bluetooth device).
The layer above is L2CAP, the Logical Link Controller Adaptation Protocol
  This acts as the data multiplexer for other layers.

## Slide 67: Bluetooth Protocol Stack - 3
Wireless Networking Standards Topic 3 - 3.67
Bluetooth Network Encapsulation Protocol
(BNEP)
  Allows the running of other networking protocols, such as IP, TCP, and UDP, over Bluetooth
RFCOMM is the virtual serial port protocol
  Allows a Bluetooth device to simulate the functions of a serial port
Service Discovery Protocol (SDP)
  Used whenever you want to find services on a remote Bluetooth device

## Slide 68: Bluetooth Protocol Stack - 4
Wireless Networking Standards Topic 3 - 3.68
The Object Exchange layer (OBEX) protocol layer
– Implemented above the RFCOMM layer and is useful when you want to transfer data as an object, such as files

## Slide 69: Bluetooth Protocol Stack - 5
Wireless Networking Standards Topic 3 - 3.69
Audio/visual control transport protocol (AVCTP) and Audio/visual data transport protocol (AVDTP)
- Used to control and distribute audio and video over Bluetooth
– Used when you want to control the functions of a media player or if you want stream audio in stereo

## Slide 70: Wireless Technologies
Wireless Networking Standards Topic 3 - 3.70
Orthogonal Frequency Division Multiplexing
Multiple Input Multiple Output
Frequency Hopping Spread Spectrum
Adaptive Frequency Hopping
Direct Sequence Spread Spectrum

## Slide 71: FDM
Wireless Networking Standards Topic 3 - 3.71
Frequency division multiplexing (FDM) is a technology that allows transmission of multiple signals simultaneously over a single transmission cable or wireless system.
Each signal travels within its own unique frequency range (carrier), which is modulated by the data (text, voice, video, etc.).

## Slide 72: OFDM
Wireless Networking Standards Topic 3 - 3.72
Orthogonal FDM is a spread spectrum technique.
Data is distributed over a large number of carriers, spaced apart at precise frequencies.
Demodulators only pick up their own frequencies and not other frequencies.
The benefits of OFDM are:
  high spectral efficiency
  resiliency to interference
  less distortion

## Slide 73: MIMO
Wireless Networking Standards Topic 3 - 3.73
Multiple Input, Multiple Output OFDM
Uses multiple antennas to simultaneously transmit/receive data
This spatial multiplexing increases data- transmission speed by a factor equal to the number of transmitting antennae
– 4 antennae = 4 x speed
All data is transmitted in the same frequency band, which utilises the spectrum very efficiently.

## Slide 74: FHSS
Wireless Networking Standards Topic 3 - 3.74
Bluetooth
Transmitter hops from frequency to frequency hundreds of times per second
Pseudo-random number generation is used to produce the sequence of frequencies.
All stations use the same seed and hop to the same frequency at the same time, thus staying synchronised.
May use TDMA or CDMA

## Slide 75: Time Division Multiple Access
Wireless Networking Standards Topic 3 - 3.75
Frequencies divided into time slots allocated to individual users.
A user is allocated a slot on a single frequency and then moved to another frequency
Several different data streams will be transmitted on one frequency in short bursts with an allocated timeslot

## Slide 76: Code Division Multiple Access
Wireless Networking Standards Topic 3 - 3.76
Each transmitter may transmit over the whole frequency spectrum all of the time.
Coding theory is used to separate all of the multiple and simultaneous transmissions.
Comparison of TDMA and CDMA
  TDMA is like a classroom where each person takes a turn to speak.
  CDMA is like a classroom of people all speaking at the same time but in different languages, so the messages are only heard by people who speak that language.

## Slide 77: AFH
Wireless Networking Standards Topic 3 - 3.77
Adaptive frequency hopping reduces interference between Bluetooth and other devices.
Transmission does not occur on channels that have significant interference.
Devices in the same frequency band and physical area detect the presence of each other and adjust their communication systems to reduce the amount of frequency overlap.

## Slide 78: DSSS
Wireless Networking Standards Topic 3 - 3.78
WLAN
Data is divided into small pieces
Each piece is allocated to a frequency channel on the available spectrum
Data is combined with a ‘chipping code’.
Chipping code helps resist interference and allows for data recovery.

## Slide 79: DSSS v FHSS
Wireless Networking Standards Topic 3 - 3.79
FHSS advantages:
  Devices are usually cheaper
  Uses less power
DSSS advantages
  Better performance
  More reliable transmission

## Slide 80: References
Wireless Networking Standards Topic 3 - 3.80
Tanenbaum, A.S. & Weatherall, D.J. (2010). Computer Networks, 5th edition. Pearson Education.
Rysavy, P. (2002). Networking Standards and Wireless Networks. Netmotion Wireless.
IEEE website: http://grouper.ieee.org/groups/802/
Bluetooth website: https://www.bluetooth.org
IBM website: http://www.ibm.com

## Slide 81: Topic 3 – Wireless Networking Standards
Wireless Networking Standards Topic 3 - 3.81
Any Questions?