## Slide 1
Computer Networks
Topic 7:
Wireless Network Hardware

## Slide 2
Computer Networks
Topic 7 – Lecture 1: Wireless Network Hardware

## Slide 3: Scope and Coverage
Wireless Network Hardware Topic 7 - 7.3
This topic will cover:
Wireless network hardware
Wireless hardware selection
Creating a wireless network

## Slide 4: Learning Outcomes
Wireless Network Hardware Topic 7 - 7.4
By the end of this topic, students will be able to:
Select the hardware component of a network
Configure the hardware components for a wireless network
Test the connectivity of a network
Troubleshoot client-side connectivity issues using appropriate tools

## Slide 5: Wireless Networks
Wireless Network Hardware Topic 7 - 7.5
Physical cabling replaced with wireless connections
Still require:
  Workstations
  Peripherals (but may be wireless)
More flexible in terms of workstation placement
Requires some hardware that is specific to wireless networks

## Slide 6: Wireless Routers
Wireless Network Hardware Topic 7 - 7.6
Support computers configured with wireless network adapters (see later)
Contain network switch to allow connection via Ethernet cable
Allow cable modem and DSL Internet connections to be shared
May include a built-in firewall

## Slide 7: Wireless Access Points
Wireless Network Hardware Topic 7 - 7.7
May join wireless clients to wired Ethernet network
May connect to another access point, or to a wired Ethernet router
In home networking, can be used to extend a network based on a wired broadband router
Clients can join the home network without re- configuring connections

## Slide 8: Business WLAN
Wireless Network Hardware Topic 7 - 7.8
Wireless access points are commonly used in large office buildings to create one WLAN.
Each access point typically supports up to 255 client computers.
By connecting access points to each other, thousands of access points can be created.
Client computers may move or "roam" between each of these access points as needed.

## Slide 9: Wireless Network Adapters
Wireless Network Hardware Topic 7 - 7.9
Allow a computing device to join a wireless LAN
Contain a built-in radio transmitter and receiver
Exist in different forms:
  PCI wireless adapters are add-in cards designed for installation inside a desktop computer having a PCI bus
  USB wireless adapters connect to the external USB port
  PC Card or PCMCIA wireless adapters insert into a narrow open bay on a notebook computer
  Most modern computers have inbuilt adapters

## Slide 10: Wireless Print Servers
Wireless Network Hardware Topic 7 - 7.10
Allows printers to be conveniently shared across a WiFi network
Usually connected to printers by a network cable, normally USB
Can connect to a wireless router over WiFi, or can be joined using an Ethernet cable
Include a built-in wireless antenna and LED lights to indicate status

## Slide 11: Wireless Print Server Advantages
Wireless Network Hardware Topic 7 - 7.11
Allows printers to be located anywhere, tied to the location of computers
Does not require a computer to manage all print jobs, that can slow down its performance
Allows administrators to change computer names and other settings without having to re-configure the network printing settings

## Slide 12: Wireless Range Extender
Wireless Network Hardware Topic 7 - 7.12
Increases the distance over which a WLAN signal can spread,
overcoming obstacles and enhancing overall network signal quality
Several different forms are available
Also known as "range expanders" or "signal boosters"

## Slide 13: Wireless Peripherals
Wireless Network Hardware Topic 7 - 7.13
A number of peripheral devices are available that can connect to a network using WiFi or Bluetooth technology and these include:
  Video cameras
  Game adapters
  Keyboard
  Mouse
  PDA
  Mobile phone

## Slide 14: Bluetooth Hardware
Wireless Network Hardware Topic 7 - 7.14
Many items that can connect to networks:
  Computer peripherals
  PDA, smartphone
  Hands free kits
  GPS
USB Bluetooth adapters used for computers that
don’t have built in Bluetooth
Bluetooth access point used for connecting to LAN via Bluetooth

## Slide 15: Bluetooth USB Adapter
Wireless Network Hardware Topic 7 - 7.15
Dongle can plug into a USB port on your PC or laptop
Comes with software required to get connected
Allows non-Bluetooth enabled PC to connect to:
  PDA/Smartphone
  GPS
  Peripherals

## Slide 16: Bluetooth Access Point
Wireless Network Hardware Topic 7 - 7.16
Can transfer data from a Bluetooth-enabled computer or device to computers connected to the LAN
Can gain Internet access through the connected LAN

## Slide 17: Ad-hoc Wireless Networks
Wireless Network Hardware Topic 7 - 7.17
Bluetooth
Device connecting directly to each other, peer-to- peer network
Generally ok for home networks
In business networks, “infrastructure mode” should
be used (access points)

## Slide 18
Computer Networks
Topic 7 – Lecture 2:
Wireless Hardware Selection & Creating a Wireless Network

## Slide 19: A Small Business Network
Wireless Network Hardware Topic 7 - 7.19
We will assume the network is being built for a small business, but the key points are relevant to any size of business.
To create a good network the basic plan is:
  Decide what kind of WLAN is needed
  Purchase the best equipment the budget allows for
  Install the equipment
  Test the installation

## Slide 20: Wireless Router
Wireless Network Hardware Topic 7 - 7.20
Provides both wireless & wired connections
Acts as bridge between LAN and WAN
Shares WAN connection between all networked computers
Acts as a DHCP server allowing each connected device to have a unique IP address
Generally contains an embedded firewall for security

## Slide 21: Choosing a Standard
Wireless Network Hardware Topic 7 - 7.21
All modern WLAN equipment support the IEEE 802.11n standard
  Maximum transfer rate 540Mbps
  Real rate less, e.g. interference and overhead
N standard equipment can usually integrate with older devices connecting at b or g standard, but will slow down entire network
Buy n standard – it can be worth upgrading old equipment

## Slide 22: Choosing Network Adapters
Wireless Network Hardware Topic 7 - 7.22
Every computer connecting to your network must have a wireless adapter.
Most new computers and other devices now come equipped with built-in wireless adapters.
Servers and other devices usually make use of built-in network Ethernet ports.
If your device has neither, purchase a wireless adapter card or USB wireless adapter.

## Slide 23: Choosing Access Points
Wireless Network Hardware Topic 7 - 7.23
A router typically has four Ethernet ports for:
  Storage devices
  Computers
  Servers
If additional ports are required, purchase additional access points.
Connecting to a router or another access point gives additional ports and enables you to add more nodes to your network.

## Slide 24: Know Your Building
Wireless Network Hardware Topic 7 - 7.24
Dense building materials reduce the strength of your wireless signal:
  Internal brick walls
Water retaining features limit the range
  Pipes
  Bathroom
May need more access points to ensure a fast, reliable connection

## Slide 25: How Many People?
Wireless Network Hardware Topic 7 - 7.25
Number of people using the network is major factor in determining number of access points
Also need adequate bandwidth
Network administrator should also be able to manage multiple access points and balance the loads
Centrally-managed wireless controller appliances can do this dynamically

## Slide 26: How Much Power?
Wireless Network Hardware Topic 7 - 7.26
Determine the number of points you need.
Then determine the power requirements necessary to support these points.
You should purchase power surge protectors for your equipment
– the most common cause of equipment failure is a power surge.

## Slide 27: Locating Access Points
Wireless Network Hardware Topic 7 - 7.27
Don't settle prematurely on a location
Install in a central location
Avoid physical obstructions
Avoid reflective surfaces
Avoid other RF transmitters
Avoid electrical equipment
Adjust antennae
Consider repeaters

## Slide 28: Don't Settle Prematurely on a Location
Wireless Network Hardware Topic 7 - 7.28
Experiment
Place the device in several different promising locations.
Not the most scientific way
Simple practical method

## Slide 29: Install in a Central Location
Wireless Network Hardware Topic 7 - 7.29
For WLANs with multiple wireless clients, find a good compromise position.
Clients too far away from the base station will manage only 10% - 50% the bandwidth of clients nearby to it
You might need to sacrifice the network performance of one client for the good of the rest of the network.

## Slide 30: Avoid Physical Obstructions
Wireless Network Hardware Topic 7 - 7.30
Barriers along the "line of sight" between client and base station will degrade the signal
Plaster or brick walls tend to have the most negative impact
Any obstruction including cabinets or furniture will weaken the signal to some degree
Obstructions tend to lie close to floor level – can install access point or router near the ceiling

## Slide 31: Avoid Reflective Surfaces
Wireless Network Hardware Topic 7 - 7.31
Some Wi-Fi signals literally bounce off:
  Windows
  Mirrors
  Metal filing cabinets
  Stainless steel counters
Reduces network range and performance

## Slide 32: Avoid Other RF Transmitters
Wireless Network Hardware Topic 7 - 7.32
At least 1m away from other appliances that send wireless signals in the same frequency range, e.g.
  Microwave ovens
  Cordless telephones
Any appliance that transmits in the same general range can generate interference

## Slide 33: Avoid Electrical Equipment
Wireless Network Hardware Topic 7 - 7.33
Other electrical equipment may generate interference:
  Electric fans
  Motors
  Flourescent lighting

## Slide 34: Adjust Antennae
Wireless Network Hardware Topic 7 - 7.34
Antennas on wireless access points and routers can usually be rotated or re-pointed to fine tune the signal
Equipment suppliers will normally include instructions on how to do this

## Slide 35: Consider Repeaters
Wireless Network Hardware Topic 7 - 7.35
If you cannot find a suitable location for your wireless gear, there are alternatives:
  Upgrade the base station antenna
  Install a Wi-Fi repeater
  Use extra access points

## Slide 36: Public or Private?
Wireless Network Hardware Topic 7 - 7.36
Decide what you wish to provide:
  Mobile and wireless access for you and your employees
  Or convenient guest access for customers and business associates
Different types of security and access controls for each

## Slide 37: Internal Private Network
Wireless Network Hardware Topic 7 - 7.37
Planning security and the logistics of connecting it to your wired network
Develop ID and authentication procedures
Create a well-defined acceptable use policy
Create a user training program
Adapting internal firewall for wireless access

## Slide 38: Public Network
Wireless Network Hardware Topic 7 - 7.38
Develop a system that automatically takes users to a log-in page
  Clearly states what can and what cannot be done while using this gateway
  Enter an email address as an acknowledgement of these public-use policies
Work with software that can lock users out of specific websites, etc.

## Slide 39: Securing Your Network
Wireless Network Hardware Topic 7 - 7.39
Have you ever searched for an unsecured wireless network when away from home or college?
Keeping the wireless network safe is a top priority
  Avoid using obsolete protocols for wireless security, like WEP (Wired Equivalent Privacy)
  WPA (Wi-Fi Protected Access) is better
  WPA2 is even better and will help safeguard against hackers

## Slide 40: Troubleshooting Your Network
Wireless Network Hardware Topic 7 - 7.40
Requires a logical approach as for wired networks
There are three main areas where problems occur:
  Workstation issues
  Access point issues
  Server/infrastructure issues

## Slide 41: The Workstation/AP interface
Wireless Network Hardware Topic 7 - 7.41
If a workstation has a problem, is it that workstation alone?
If only one workstation has a problem and other workstations function, the problem is with the workstation.
If the problem is with all workstations, the problem lies with the access point.

## Slide 42: The AP/Wired LAN interface
Wireless Network Hardware Topic 7 - 7.42
Use a wired workstation to ping the access point that has a problem.
If ping is successful, the problem is likely to lie with the wired network
If ping is unsuccessful, then the AP is not connected and there is a problem with the AP or the wired connection from AP

## Slide 43: References
Wireless Network Hardware Topic 7 - 7.43
Lowe, D. (2009). Networking for Dummies, 9th edition. John Wiley & Sons.
Rackley, S. (2007). Wireless Networking Technology: From Principles to Successful Implementation. Newnes.

## Slide 44: Topic 7 – Wireless Network Hardware
Wireless Network Hardware Topic 7 - 7.44
Any Questions?