## Slide 1
Computer Networks
Topic 9: Firewalls

## Slide 2
Computer Networks
Topic 9 – Lecture 1: Functions of a Firewall

## Slide 3: Scope and Coverage
Firewalls Topic 9 - 9.3
This topic will cover:
Functions of a firewall
Types of firewall
Installing and configuring a firewall

## Slide 4: Learning Outcomes
Firewalls Topic 9 - 9.4
By the end of this topic, students will be able to:
Describe the functions of a firewall
Describe different types of firewall
Install and configure a firewall on an Internet- connected system

## Slide 5: What is a Firewall?
Firewalls Topic 9 - 9.5
In the industrial world, it is a solid wall that has been built to contain a fire
– For example, an area of a chemical plant will have a firewall to contain any fire that may break out.
In computing, a firewall is built to protect a network.
The aim is to protect the network from malicious traffic.

## Slide 6: Network Firewall
Firewalls Topic 9 - 9.6
A firewall is the first line of defence for your network.
The purpose of a firewall is to keep intruders from gaining access to your network.
Usually placed at the perimeter of network to act as a gatekeeper for incoming and outgoing traffic
It protects your computer from Internet threats by erecting a virtual barrier between your network or computer and the Internet

## Slide 7: How Does a Firewall Work?
Firewalls Topic 9 - 9.7
Examines the traffic sent between two networks
  e.g. examines the traffic being sent between your network and the Internet
Data is examined to see if it appears legitimate:
  if so, the data is allowed to pass through
  If not, the data is blocked
A firewall allows you to establish certain rules to determine what traffic should be allowed in or out of your private network.

## Slide 8: What Are The Rules?
Firewalls Topic 9 - 9.8
Each organisation has to decide on the level of security they require
– There is no “one size fits all” solution
Firewalls can be configured to allow or block traffic based upon rules.
Software firewalls often come with a set of preconfigured options based upon the security level required.
Can usually be configured rule by rule

## Slide 9: What to Block
Firewalls Topic 9 - 9.9
Traffic blocking rules can be based upon:
  Words or phrases
  Domain names
  IP addresses
  Ports
  Protocols (e.g. FTP)
While firewalls are essential, they can block legitimate transmission of data and programs.

## Slide 10: Words, Phrases & Domain Names
Firewalls Topic 9 - 9.10
Lists of words and phrases that are not allowed can be used to block traffic
  There can be problems when a legitimate word contains a blocked word within it.
Similarly, lists of domain names can be used to block traffic
  Could be a blocked list where access is prevented
  Could be an allowed list and access is only allowed to domains on the list and nothing else

## Slide 11: IP Addresses & Ports
Firewalls Topic 9 - 9.11
A firewall typically filters information by examining
I.P. addresses and port information.
The firewall can determine which ports and I.P. addresses are normal.
It keeps a list of situations that are suspicious.
If something looks suspicious, it will stop the flow of data.

## Slide 12: Source & Destination IP Address - 1
Firewalls Topic 9 - 9.12
Some firewalls can filter traffic based on source or destination IP address.
Enables you to allow or deny traffic based on the computers or networks that are sending or receiving the traffic
  Can configure firewalls to block specific websites
  Can allow/deny traffic based on the sending computer
  Can disable a protocol on one set of computers and allow the same protocol on a different set of computers

## Slide 13: Source & Destination IP Address - 2
Firewalls Topic 9 - 9.13
Allows you to give greater access to users on internal networks than those on external networks
  Common to use a firewall to block all requests sent to an internal email server except those requests from users on the internal network
Can also use source filtering to block all requests from a specific address
  e.g. to block traffic from an IP address identified as having attacked the network

## Slide 14: Protocols
Firewalls Topic 9 - 9.14
Firewalls can also filter traffic based on protocol
  this option is not usually enabled by default.
This allows an organisation to block all traffic of a particular type
  A business might have a firewall block HTTP traffic to prevent employees from accessing the Internet while at work.
  A business may block all FTP traffic to prevent files being uploaded or downloaded.

## Slide 15: Common Firewall Types
Firewalls Topic 9 - 9.15
In general, there are software firewalls and
hardware firewalls
– Even in home networks
Hardware firewalls are typically found in routers, which distribute incoming traffic from an Internet connection to computers.
Software firewalls reside in individual computers.
Ideally, a network should have both.

## Slide 16: Software Firewall
Firewalls Topic 9 - 9.16
Protects only the computer on which they are installed
Provides excellent protection against threats (viruses, worms, etc.)
Has a user-friendly interface
Has flexible configuration

## Slide 17: Router Firewall
Firewalls Topic 9 - 9.17
Protects your entire network or part of a network
Located on your router
Protects network hardware which cannot have a software firewall installed on it
Allows the creation of network-wide rules that govern all computers on the network

## Slide 18: Do You Need a Firewall?
Firewalls Topic 9 - 9.18
The answer is always YES
– Unless you never connect to an outside network
Firewalls are a critical part of Internet security.
It is recommended that all computers have a software firewall.
Firewalls can be found in all commercial Internet security suites.

## Slide 19
Computer Networks
Topic 9 – Lecture 2: Types of Firewall

## Slide 20: Types of Firewall
Firewalls Topic 9 - 9.20
Can be divided into three main types:
  Packet filters
  Application gateways
  Packet inspection
Individual vendors of firewalls may provide additional features
  You should look at their products for details

## Slide 21: What do Packet Filters Examine?
Firewalls Topic 9 - 9.21
Packet-filtering firewalls validate individual packets based on:
  Protocol
  Source and/or destination IP address
  Source and/or destination port numbers
  Time range
  Type of service (ToS)
  Various other parameters within the IP header

## Slide 22: Access Control Lists
Firewalls Topic 9 - 9.22
Packet filtering is generally accomplished using Access Control Lists (ACL) on routers or switches.
Normally very fast
  Traffic enters or exits an interface
  ACLs are used to match selected criteria
  Either permit or deny individual packets

## Slide 23: Advantages of Packet Filters
Firewalls Topic 9 - 9.23
Big advantage is that they are present in many networked devices
Packet-filtering firewalls are located in:
  Routers
  Switches
  Wireless access points
Routers have the capability to control the flow of packets through the use of ACLs

## Slide 24: Does My Network Use Packet Filters?
Firewalls Topic 9 - 9.24
Almost certainly (or it should!)
These devices do not have lots of features.
But when you need to quickly implement a security policy, this may be the quickest solution to deploy:
  to mitigate an attack
  protect against infected devices
  etc.

## Slide 25: Problems With Packet Filters
Firewalls Topic 9 - 9.25
Packet filtering can be circumvented in a number of ways including:
  Misrepresenting traffic using well-known port numbers
  Tunnelling traffic unsuspectingly within traffic allowed by the ACL rules
It was quickly discovered that peer-to-peer sharing applications could use port 80 (HTTP) to gain access through the firewall.

## Slide 26: Using Packet Filters
Firewalls Topic 9 - 9.26
Packet filters alone are insufficient
Multiple devices can provide defence in depth
Packet filtering is best used on the outer edge of your network
Can prevent spoofed traffic and private IP addresses from entering or exiting your network

## Slide 27: The OSI Application Layer
Firewalls Topic 9 - 9.27
Application Gateways, or Application Layer Firewalls, work at the application layer of the OSI model.
Layer 7, the application layer
– It is the user interface to your computer (the programs), for example, word processor, email application, telnet, and so on.
We include “proxies” in this category of firewalls.

## Slide 28: Application Gateways
Firewalls Topic 9 - 9.28
Application-layer firewalls can understand the traffic flowing through them and allow or deny traffic based on the content.
Host-based firewalls designed to block objectionable Web content based on keywords are a form of application-layer firewall.
Application-layer firewalls can inspect packets bound for an internal Web server to ensure the request isn’t really an attack in disguise.

## Slide 29: Proxies
Firewalls Topic 9 - 9.29
A proxy device may be dedicated hardware (e.g. a server) or software.
Acts as a firewall by responding to input packets (connection requests, for example) in the manner of an application, whilst blocking other packets
Make tampering with an internal system from the external network more difficult
Act on behalf of a client so they provide an additional buffer to the network

## Slide 30: Advantages
Firewalls Topic 9 - 9.30
Provide a buffer from port scans and application attacks
  If an attacker finds a vulnerability in an application, the attacker would have to compromise the application/proxy firewall before attacking devices behind the firewall
Can be patched quickly in the event of a vulnerability being discovered
  This may not be true for patching all the internal devices

## Slide 31: Disadvantages
Firewalls Topic 9 - 9.31
Needs to know how to handle traffic to and from your specific application
  If you have an application that's unique, your proxy firewall may not be able to support it without making some significant modifications
Application firewalls are generally much slower than packet-filtering or packet-inspection firewalls
  They run applications, maintain state for both the client and server, and also perform inspection of traffic

## Slide 32: Packet Inspection Firewalls
Firewalls Topic 9 - 9.32
Examine the session information between devices:
  Protocol
  New or existing connection
  Source IP address
  Destination IP address
  Port numbers
  IP checksum
  Sequence numbers
  Application-specific information

## Slide 33: Outbound Internet Traffic
Firewalls Topic 9 - 9.33
Client initiates connection to IP address of the web server destined for port 80 (HTTP)
Firewall determines whether that packet is allowed through the firewall based on the current rule-set
Firewall looks into the data portion of the IP packet and determines whether it is legitimate HTTP traffic
If all the requirements are met, a flow entry is created in the firewall based on the session information, and that packet is allowed to pass.

## Slide 34: Inbound Internet Traffic
Firewalls Topic 9 - 9.34
Web server receives the packet and responds
Return traffic is received by the firewall
Firewall determines if return traffic is allowed by comparing the session information with the information contained in the local translation table
If return traffic matches the previous requirements, payload is inspected to validate appropriate HTTP
Then it is forwarded to the client

## Slide 35: Advantages
Firewalls Topic 9 - 9.35
Generally much faster than application firewalls
  They are not required to host client applications
Most of the packet-inspection firewalls today also offer deep-packet inspection
  The firewall can dig into the data portion of the packet and also:
  Match on protocol compliance
  Scan for viruses
  Still operate very quickly

## Slide 36: Disadvantages
Firewalls Topic 9 - 9.36
Open to certain denial-of-service attacks
These can be used to fill the connection tables with illegitimate connections.

## Slide 37: Network Address Translation (NAT)
Firewalls Topic 9 - 9.37
Firewalls often have NAT functionality
Hosts behind a firewall commonly have addresses in a private address range.
Hides the true address of protected hosts
Hiding the addresses of protected devices is a defence against network reconnaissance.

## Slide 38
Computer Networks
Topic 9 – Lecture 3:
Installing and Configuring a Firewall

## Slide 39: Planning the Firewall
Firewalls Topic 9 - 9.39
A number of factors must be considered before purchasing and installing a firewall or firewalls:
  Firewall policy
  Risk analysis
  Identifying requirements
  Creating rules
  Managing the firewall

## Slide 40: Firewall Policy
Firewalls Topic 9 - 9.40
Defines how an organisation’s firewalls should handle inbound and outbound network traffic, based on the organisation’s information security policies, for:
  Specific IP addresses
  IP address ranges
  Protocols
  Applications
  Content types

## Slide 41: Risk Analysis
Firewalls Topic 9 - 9.41
Organisations should conduct risk analysis to develop a list of:
  The types of traffic needed by the organisation
  How they must be secured
  Which types of traffic and under what circumstances
All inbound and outbound traffic not expressly permitted should be blocked.
This reduces the risk of attack and can decrease the volume of traffic on the network.

## Slide 42: Identifying Requirements
Firewalls Topic 9 - 9.42
Which network areas need to be protected?
Which firewall technologies will be most effective for the types of traffic that require protection?
Integrating the firewall into existing network and security infrastructures
Requirements relating to physical environment and personnel
Consideration of possible future needs

## Slide 43: Creating Rules
Firewalls Topic 9 - 9.43
Implement the firewall policy and support firewall performance
Rulesets should be as specific as possible with regards to the network traffic they control:
  Types of traffic
  Protocols
The details of creating rulesets vary widely by type of firewall and specific products.

## Slide 44: Managing the Firewall
Firewalls Topic 9 - 9.44
Policy rules need to be updated as the
organisation’s requirements change.
Firewall performance needs to be monitored.
Logs and alerts should also be continuously monitored to identify threats.
Rulesets and policies should be managed by a formal change management control process.
Firewall software should be patched as vendors provide updates to address vulnerabilities.

## Slide 45: Small Networks
Firewalls Topic 9 - 9.45
Firewalls at a network’s perimeter provide some
measure of protection for internal hosts.
Network firewalls are not able to recognise all forms of attack, some reach internal hosts.
Attacks sent from one internal host to another may not even pass through a network firewall.
Network designers include firewall functionality at places other than the network perimeter to provide an additional layer of security.

## Slide 46: Host Based Firewalls - 1
Firewalls Topic 9 - 9.46
Firewalls for servers and personal firewalls for desktop and laptop computers
Provide an additional layer of security
Software-based, residing on the hosts they are protecting
Monitor and control the incoming and outgoing network traffic for a single host

## Slide 47: Host Based Firewalls - 2
Firewalls Topic 9 - 9.47
May come with OS
Can be installed as third-party add-on
Perform logging
Can be configured to perform address-based and application-based access controls
Can also act as intrusion prevention systems that detect an attack in progress and take action to prevent damage to the targeted host

## Slide 48: Demilitarised Zones (DMZ) - 1
Firewalls Topic 9 - 9.48
Traffic moving between the DMZ and other interfaces on the protected side of the firewall still goes through the firewall
This traffic has firewall protection policies applied
Common to put public-facing servers on the DMZ:
  Web servers
  Email servers

## Slide 49: Demilitarised Zones (DMZ) - 2
Firewalls Topic 9 - 9.49

## Slide 50: Multiple Firewall Layers
Firewalls Topic 9 - 9.50
Firewalls should be at the edge of a logical network boundary.
A network administrator may wish to have additional boundaries within the network.
Can deploy additional firewalls to establish such boundaries
The use of multiple layers of firewalls is quite common to provide defence-in-depth.

## Slide 51: Many Layers of Trust
Firewalls Topic 9 - 9.51
Internal users may have varying levels of trust
  Accounting databases may only allow access by members of the accounting department
  Many organisations deploy specific wireless access points within their networks for visitor use
Have one firewall at the edge of the network and another at the edge of the internal network that has extra protection

## Slide 52: Problems with Multiple Layers
Firewalls Topic 9 - 9.52
Increased difficulty in tracing firewall problems
Multiple layers of application/proxy gateways is problematic as each can change a message, which makes debugging even more difficult.

## Slide 53: Planning and Implementation
Firewalls Topic 9 - 9.53
The lifecycle is:
Plan
Configure
Test
Deploy
Manage

## Slide 54: Plan
Firewalls Topic 9 - 9.54
Should consider:
  Security Capabilities
  Management
  Performance
  Integration
  Physical Environment
  Personnel
  Future Needs

## Slide 55: Configure
Firewalls Topic 9 - 9.55
This includes:
  Installing hardware
  Installing software
  Configuring policies
  Configuring logging and alerting
  Integrating the firewall into the network architecture
The details of creating a ruleset vary by type of firewall and specific products.

## Slide 56: Test
Firewalls Topic 9 - 9.56
A number of features should be tested:
  Connectivity
  Ruleset
  Application compatibility
  Management
  Logging
  Performance
  Interoperability
  Any additional features

## Slide 57: Deploy
Firewalls Topic 9 - 9.57
Administrators should notify users of the planned deployment
Involves integrating the firewall with other network elements
Has to be integrated into the routing structure
Can mean changing the routing tables for other routers in the network
If elements in the network use dynamic routing, they may need to have their configuration modified

## Slide 58: Manage
Firewalls Topic 9 - 9.58
The longest lasting phase
Managing the solution involves maintaining:
  Firewall architecture
  Policies
  Software
  Other components of the solution
Review the firewall policy at regular intervals

## Slide 59: References
Firewalls Topic 9 - 9.59
Price B. (ed) (2003). Networking Complete, 3rd edition, Sybex.
Tanenbaum, A.S. & Weatherall, D.J. (2010). Computer .Networks, 5th edition, Pearson Education.

## Slide 60: Topic 9 – Firewalls
Firewalls Topic 9 - 9.60
Any Questions?